## WELDING, CUTTING AND BRAZING

- Are only authorized and trained personnel permitted to use welding, cutting or brazing equipment?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Does each operator have a copy of the appropriate operating instructions and are they directed to follow them?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are compressed gas cylinders regularly examined for obvious signs of defects, deep rusting, or leakage?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Is care used on handling and storage of cylinders, safety valves, relief valves, etc., to prevent damage?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are oxygen cylinders in storage separated from fuel-gas cylinders or combustible materials (especially oil or grease), a minimum distance of 20 feet or by a noncombustible barrier at least 5 feet high having a fire-resistance rating of at least one-half hour?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are only approved apparatus (torches, regulators, pressure-reducing valves, acetylene generators, manifolds) used?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are cylinders kept away from sources of heat?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are the cylinders kept away from elevators, stairs, or gangways?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Is it prohibited to use cylinders as rollers or supports?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are empty cylinders appropriately marked and their valves closed?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are signs reading: DANGER - NO SMOKING, MATCHES, OR OPENLIGHTS, or the equivalent, posted?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are cylinders, cylinder valves, couplings, regulators, hoses, and apparatus kept free of oily or greasy substances?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Is care taken not to drop or strike cylinders?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Unless secured on special trucks, are regulators removed and valve-protection caps put in place before moving cylinders?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Do cylinders without fixed hand wheels have keys, handles, or non-adjustable wrenches on stem valves when in service?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are liquefied gases stored and shipped valve-end up with valve covers in place?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are provisions made to never crack a fuel-gas cylinder valve near sources of ignition?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Before a regulator is removed, is the valve closed and gas released from the regulator?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Is red used to identify the acetylene (and other fuel-gas) hose, green for oxygen hose, and black for inert gas and air hose?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are pressure-reducing regulators used only for the gas and pressures for which they are intended?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Is open circuit (No Load) voltage of arc welding and cutting machines as low as possible and not in excess of the recommended limits?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Under wet conditions, are automatic controls for reducing no load voltage used?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Is grounding of the machine frame and safety ground connections of portable machines checked periodically?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are electrodes removed from the holders when not in use?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Is it required that electric power to the welder be shut off when no one is in attendance?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Is suitable fire extinguishing equipment available for immediate use?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Is the welder forbidden to coil or loop welding electrode cable around his body?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are wet machines thoroughly dried and tested before being used?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are work and electrode lead cables frequently inspected for wear and damage, and replaced when needed?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Do means for connecting cable lengths have adequate insulation?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- When the object to be welded cannot be moved and fire hazards cannot be removed, are shields used to confine heat, sparks, and slag?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are firewatchers assigned when welding or cutting is performed in locations where a serious fire might develop?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are combustible floors kept wet, covered by damp sand, or protected by fire-resistant shields?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- When floors are wet down, are personnel protected from possible electrical shock?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- When welding is done on metal walls, are precautions taken to protect combustibles on the other side?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Before hot work is begun, are used drums, barrels, tanks, and other containers so thoroughly cleaned that no substances remain that could explode, ignite, or produce toxic vapors?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Is it required that eye protection helmets, hand shields and goggles meet appropriate standards?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are employees exposed to the hazards created by welding, cutting, or brazing operations protected with personal protective equipment and clothing?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Is a check made for adequate ventilation in and where welding or cutting is performed?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- When working in confined places, are environmental monitoring tests taken and means provided for quick removal of welders in case of emergency?

Action to be Taken						Assigned To:

_____________________________________   ____________________________