ABRASIVE WHEEL EQUIPMENT-GRINDERS

- Is the work rest used and kept adjusted to within 1/8 inch of the wheel?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Is the adjustable tongue on the topside of the grinder used and kept adjusted to within 1/4 inch of the wheel?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Do side guards cover the spindle, nut, and flange and 75 percent of the wheel diameter?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are bench and pedestal grinders permanently mounted?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are goggles or face shields always worn when grinding?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Is the maximum RPM rating of each abrasive wheel compatible with the RPM rating of the grinder motor?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are fixed or permanently mounted grinders connected to their electrical supply system with metallic conduit or other permanent wiring method?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Does each grinder have an individual on and off control switch?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Is each electrically operated grinder effectively grounded?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Before new abrasive wheels are mounted, are they visually inspected and ring tested?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are dust collectors and powered exhausts provided on grinders used in operations that produce large amounts of dust?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are splashguards mounted on grinders that use coolant to prevent the coolant reaching the employees?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Is cleanliness maintained around grinders?

Action to be Taken						Assigned To:

_____________________________________   ____________________________