## HOIST AND AUXILIARY EQUIPMENT

- Is each overhead electric hoist equipped with a limit device to stop the hook travel at its highest and lowest point of safe travel?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Will each hoist automatically stop and hold any load up to 125 percent of its rated load if its actuating force is removed?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Is the rated load of each hoist legibly marked and visible to the operator?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are stops provided at the safe limits of travel for trolley hoist?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are the controls of hoist plainly marked to indicate the direction of travel or motion?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Is each cage-controlled hoist equipped with an effective warning device?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are close-fitting guards or other suitable devices installed on hoist to assure hoist ropes will be maintained in the sheave grooves?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are all hoist chains or ropes of sufficient length to handle the full range of movement of the application while still maintaining two full wraps on the drum at all times?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are nip points or contact points between hoist ropes and sheaves which are permanently located within seven feet of the floor, ground or working platform, guarded?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Is it prohibited to use chains or rope slings that are kinked or twisted?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Is it prohibited to use the hoist rope or chain wrapped around the load as a substitute, for a sling?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Is the operator instructed to avoid carrying loads over people?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are only employees who have been trained in the proper use of hoists allowed to operate them?

Action to be Taken						Assigned To:

_____________________________________   ____________________________