PORTABLE (POWER OPERATED) TOOLS AND EQUIPMENT

- Are grinders, saws and similar equipment provided with appropriate safety guards?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are power tools used with the correct shield, guard, or attachment, recommended by the manufacturer?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are portable circular saws equipped with guards above and below the base shoe?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are circular saw guards checked to assure they are not wedged up, thus leaving the lower portion of the blade unguarded?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are rotating or moving parts of equipment guarded to prevent physical contact?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are all cord-connected, electrically operated tools and equipment effectively grounded or of the approved double insulated type?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are effective guards in place over belts, pulleys, chains, sprockets, on equipment such as concrete mixers, air compressors, etc.?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are portable fans provided with full guards or screens having openings 1/2 inch or less?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Is hoisting equipment available and used for lifting heavy objects, and are hoist ratings and characteristics appropriate for the task?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are ground-fault circuit interrupters provided on all temporary electrical 15 and 20-ampere circuits, used during periods of construction?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are pneumatic and hydraulic hoses on power-operated tools checked regularly for deterioration or damage?

Action to be Taken						Assigned To:

_____________________________________   ____________________________

- Are precautions taken when using fuel-powered tools in enclosed spaces?

Action to be Taken						Assigned To:

_____________________________________   ____________________________